## Slide 1
John McCloskey
NASA/GSFC Chief EMC Engineer
Code 565
301-286-5498
John.C.McCloskey@nasa.gov
Effects of Rise/Fall Times
on Signal Spectra

## Slide 2: Purpose of Demo/Tutorial
Demonstrate the relationship between time domain and frequency domain representations of signals
In particular, demonstrate the relationship between rise/fall times of digital clock-type signals and their associated spectra
Fast rise/fall times can produce significant high frequency content out to 1000th harmonic and beyond
  Common cause of radiated emissions that can interfere with on-board receivers
  Can be reduced by limiting rise/fall times

## Slide 3: Topics
Sinusoid: Time Domain vs. Frequency Domain
Fourier series expansions of:
  Square wave
  Rectangular pulse train
  Trapezoidal waveform
Comparison to measured results for these waveforms
Observations

## Slide 4: Sinusoid: Time Domain vs. Frequency Domain
TIME DOMAIN
FREQUENCY DOMAIN
Frequency
Amplitude
A
f

## Slide 5: Fourier Series Expansion of Signal Waveforms
Recommended reading for an in-depth look at Fourier series expansions of signal waveforms:
  Clayton Paul, “Introduction to Electromagnetic Compatibility,” sections 3.1 and 3.2

## Slide 6: Fourier Series Expansion of Square Wave
Odd harmonics only

## Slide 7: Fourier Series Expansion of Rectangular Pulse Train
sin(x)/x
(next slide)
Even harmonics included
NOTE: For 50% duty cycle (τ/T = 0.5), this equation reduces to that for the square wave on the previous slide.

## Slide 8: Response and Envelope of sin(x)/x
Envelope of |sin(x)/x|:
1 for x < 1
1/x for x > 1
Response of |sin(x)/x|:
0 for x = nπ
1/x for x = (n+1)π/2
Lines meet at x = 1

## Slide 9: Envelope of Rectangular Pulse Train Spectrum
f
0 dB/decade
-20 dB/decade
PULSE WIDTH
f1
f2
f3
f4
f5
etc…
DC offset
Low frequency “plateau”
Harmonic response

## Slide 10: Fourier Series Expansion of Trapezoidal Waveform
Additional sin(x)/x term due to rise/fall time
τ
τr
τf
T
A
Assume τr = τf :
NOTE: τr and τf are generally measured between 10% and 90% of the minimum and maximum values of the waveform.

## Slide 11: Envelope of Trapezoidal Waveform Spectrum
f
0 dB/decade
-20 dB/decade
-40 dB/decade
PULSE WIDTH
RISE/FALL TIME
DC offset
Low frequency “plateau”
Harmonic response
(pulse width)
Harmonic response
(rise/fall time)
f1
f2
f3
f4
f5
etc…

## Slide 12: Trapezoidal Waveform Spectrum (Simplified)
f
0 dB/decade
-20 dB/decade
-40 dB/decade
PULSE WIDTH
RISE/FALL TIME
Slower rise/fall times provide additional roll-off of higher order harmonics

## Slide 13: Test Setup
WAVETEK 801 pulse generator
TEKTRONIX DPO7054 oscilloscope
(1 MΩ input)
TEKTRONIX RSA5103A spectrum analyzer
(50 Ω input)

## Slide 14: Applied Waveform
τ
τr
τf
T
A
A = 1 V
T = 200 µs
(f0 = 5 kHz)
τ, τr , & τf varied as indicated on following slides

## Slide 15: τ = 100 µs; τr = τf = 40 ns
τ/T = 50%
2A(τ/T) = 1 V
= 120 dBµV

## Slide 16: τ = 100 µs; τr = τf = 360 ns
2A(τ/T) = 1 V
= 120 dBµV
τ/T = 50%

## Slide 17: τ = 100 µs; τr = τf = 3.6 µs
2A(τ/T) = 1 V
= 120 dBµV
τ/T = 50%

## Slide 18: τ = 100 µs; τr = τf = 10 µs
2A(τ/T) = 1 V
= 120 dBµV
τ/T = 50%

## Slide 19: τ = 80 µs; τr = τf = 40 ns
2A(τ/T) = 0.8 V
= 118 dBµV
τ/T = 40%

## Slide 20: τ = 80 µs; τr = τf = 360 ns
2A(τ/T) = 0.8 V
= 118 dBµV
τ/T = 40%

## Slide 21: τ = 80 µs; τr = τf = 3.3 µs
2A(τ/T) = 0.8 V
= 118 dBµV
τ/T = 40%

## Slide 22: τ = 80 µs; τr = τf = 10 µs
2A(τ/T) = 0.8 V
= 118 dBµV
τ/T = 40%

## Slide 23: τ = 10 µs; τr = τf = 40 ns
2A(τ/T) = 0.1 V
= 100 dBµV
τ/T = 5%

## Slide 24: τ = 10 µs; τr = τf = 350 ns
2A(τ/T) = 0.1 V
= 100 dBµV
τ/T = 5%

## Slide 25: τ = 10 µs; τr = τf = 2 µs
2A(τ/T) = 0.1 V
= 100 dBµV
τ/T = 5%

## Slide 26: τ = 2 µs; τr = τf = 160 ns
2A(τ/T) = 0.02 V
= 86 dBµV
τ/T = 1%

## Slide 27: τ = 2 µs; τr = τf = 20 ns
2A(τ/T) = 0.02 V
= 86 dBµV
τ/T = 1%

## Slide 28: τ = 2 µs; τr = τf = 400 ns
2A(τ/T) = 0.02 V
= 86 dBµV
τ/T = 1%

## Slide 29: τ = 100 ns; τr = τf = 8 ns
2A(τ/T) = 1 mV
= 60 dBµV
τ/T = 0.05%

## Slide 30: Observations (1 of 2)
Measured spectra show good agreement with expected values
  “3-line” envelope provides simple, accurate, and powerful analytical tool for correlating signal spectra to trapezoidal waveforms
Even harmonics
  Reduced, but not zero, amplitude for 50% duty cycle
  Varying amplitude for other than 50% duty cycle
  Must be considered as potentially significant contributors to spectrum
Low frequency plateau scales with duty cycle
  Spectrum for low duty cycle waveforms gives artificial indication of low amplitude
  First “knee” frequency may be quite high, producing relatively flat spectrum for many harmonics (100s or 1000s in these examples)
  Low duty cycle waveforms should be observed in time domain (oscilloscope) as well as frequency domain (spectrum analyzer)

## Slide 31: Observations (2 of 2)
Signal spectra significantly more determined by rise/fall times than by fundamental frequency of waveform
Uncontrolled rise/fall times can produce significant frequency content out to 1000th harmonic and beyond
  Common cause of radiated emissions
  5 MHz clock can easily produce harmonics out to 5 GHz and beyond
  Potential interference to S-band receiver (~2 GHz), GPS (~1.5 GHz), etc.
Controlling rise/fall times can significantly limit high frequency content at source
LIMIT THOSE RISE/FALL TIMES!!!

## Slide 32: Questions/Comments
Contact:
  John McCloskey
  NASA/GSFC Chief EMC Engineer
  Phone: 301-286-5498
  E-mail: John.C.McCloskey@nasa.gov